## Slide 1: Parallel Transmit, from fields to excitations to sequences
Prof Shaihan Malik

## Slide 2: Control of imperfections
‘Self learning’ can be a way to overcome system imperfections
The radiofrequency (RF) magnetic field = field can be non-uniform
We consider ways to overcome this specific problem as an example in this talk

## Slide 3: B1 inhomogeneity
  Problematic for clinical 3T imaging
  Variability between subjects
  Effects get worse as B0 increases
Cardiac (short axis)
Thighs (coronal view)
Foetus (in utero)
Breast (axial view)
7T Brain image
Notes: About 10% of whole body scanners (~400 total), but 20-30% of new installs
3Ts now in NHS trusts country wide

## Slide 4: What is parallel transmission?
0
90
‘Transmission’ = Generate RF magnetic field (‘B1’)
B1 field not spatially uniform at high field (3T+)
Spatial properties depend on EM interaction between body and coil – we cannot control this.
b(t)
B1 during RF pulse at 3T
Standard, single channel transmission

## Slide 5: Parallel Transmission
0
90
Move from large resonator with single input to an array of smaller coils with their own RF amplifier
Schematic closely resembles an old experimental 3T pTx body array but can be any array coil

## Slide 6: Parallel Transmission
Move from large resonator with single input to an array of smaller coils with their own RF amplifier
Key property: Each coil can be driven with separate RF waveform
Modern commercial 3T systems often use 2-port birdcage coils
Clement et al, MRM 2019;81:1447-1458

## Slide 7: Parallel Transmission: spatial & temporal control
PTx allows spatial and temporal control of the B1 field
By controlling the inputs on each coil separately we can make B1 vary in space and time. But how to use these degrees of freedom?
Parallel transmission:
bi(t)
RF magnetic field: B1

## Slide 8: RF shimming (aka ‘static’ pTx)
RF shimming is the simplest and most common application of PTx
find time independent weights
Independent of pulse sequence
Performance depends on field patterns produced by individual coils:
          Number of coils
          Coil design

## Slide 9: From Fields to Excitations (‘dynamic’ pTx)
B1 field is used to excite magnetization
  Integrate the Bloch equation through time to predict ‘excitation’ properties
  ‘Small tip angle’1 => Fourier approximation …
Contains and including gradients
F
b
S
m
=
1Pauly et al, JMR 1989 81(1):43

## Slide 10: From Fields to Excitations (‘dynamic’ pTx)
With pTx generalise this to multiple channels
Can apply to multidimensional RF pulses where the selection gradient is on multiple axes…
m = S1F … SRF
b1
bR
…
Grissom et al 2006
m = Ab
Ab - m
2
W
+ λ b
2
min
b
‘artistic’ images of water phantoms are a common demonstration…
1Malik & Hajnal, MRM 2016 76(3):848
Notes: PULSED B1 field
My papers – pioneering translational work

## Slide 11: B1 Homogeneity correction
Can use same machinery to produce spatially uniform excitations from non-uniform fields
Example: T1w volumetric imaging at 3T with MP-RAGE …
Typical B1 variation at 3T
‘centre brightening’ artefact

## Slide 12: SPINS Pulse waveforms
RF pulse waveforms
B1 field during transmission
(each colour is a different transmit channel)
We conceptualize our design as a sum of excitations from independent channels
But in reality we produce a single spatio-temporally variable field which makes the excitation

## Slide 13: SPINS Results (3T)
Images used the the ADNI MP-RAGE sequence
Signal change
+40%
+20%
0%
-20%
-40%

## Slide 14: Whole sequence design: Direct Signal Control
milliseconds to seconds
s - ms
Conventional Pulse Sequence
Signal depends on interactions between pulses and spin system potentially over timescale of entire scan
Parallel TX channels

## Slide 15: Whole sequence design: Direct Signal Control
Subject-Specific
Signal Model
(measured B1 maps & sequence properties)
Numerical Optimization
Dynamically control RF on intermediate timescale to control signal evolution
Malik et al, MRM 2012 68(5):1481
Parallel TX channels

## Slide 16: From excitation to signal model
Spatially resolved EPG
Classical non-linear optimization
A is a matrix of all flip angles across all channels, therefore contains all possible FSE variants1-4
      Find local solutions => start point important
f({α0,α1,α2,… αn},T1,T2)
f({α0(r),α1(r),α2(r),… αn(r)},T1(r),T2(r))
Target signal (for each echo & voxel)
SR-EPG prediction
S(r) = f(A)
Regularization for total RF power
Weighting term
|S(r)| - T(r)
2
W(r)
+ λ A
2
min
A
∑
r∊Ω

## Slide 17: Direct Signal Control: example
Multi-shot FSE example
“A bit like MR Fingerprinting in reverse”
Predicted Signals (Spatially Resolved-EPG)
Direct Signal Control
CP mode
‘uniform field’
RF Shim
Images windowed identically
Malik et al, MRM 2012 68(5):1481

## Slide 18: Direct Signal Control : TSE imaging at 7T
Original
DSC
High resolution FSE (0.3x0.3x1.2mm3). ETL=9
7T with 8-ch PTx
Sbrizzi et al, MRM 2017 77:361-373

## Slide 19: Different time-frames of control
Static => consider the fields
Dynamic (single pulse) => consider the magnetization
Dynamic (multi-pulse) => consider the signal
Each has their own use cases!

## Slide 20: Do we always need to optimize?
’Universal’ pulse designs1 – good performance achieved by ‘training’ on B1 data from multiple subjects
‘Hybrid’ universal / individual optimization (‘FOCUS’ pulse design2) provides refinement
1Gras et al, MRM 2017 77 (2):635
2Herrler et al, MRM 2021 85:3140

## Slide 21: Outlook
pTx gives spatial and temporal control of RF fields
Optimal method really depends on the application (not ‘one size fits all’)
Classic approaches are optimization based, but ‘learning’ is coming
        ‘universal’ solutions are a low-order type of learning
        More bespoke methods are being researched

## Slide 22: Thank you
Shaihan.malik@kcl.ac.uk https://www.kcl.ac.uk/people/shaihan-malik
© 2020 King’s College London. All rights reserved